## Slide 1: Configuring Server to communicate with CET meters (Ethernet)
CET Inc.
www.cet-global.com

## Slide 2: Contents
Configuring the Meter Settings
    1. Connect to meter
    2. View server network information
    3. Configure meter communication settings
Verifying the Communication
    Ping meter IP
    Troubleshooting

## Slide 3: Configuring the Meter Settings

## Slide 4: 1. Connect to meter
Make sure the Ethernet cable plug in the right port corresponding to meter settings.
Select a port to connect
·
Picture.1 Some meters have 2 port available

## Slide 5: 2. View server network information
WinKey + R on your keyboard. Or you could open the start menu and type Run.
Open network and sharing center
1)
1
1
2
Enter control in the Run Command box followed by the Return key.
3
Now Control Panel come out, click to enter Network and Sharing Center.
3
2

## Slide 6: 2. View server network information
Click Ethernet of the View your active networks list.
Check the network information
2)
1
2
Click Details… under General tab.
3
Check the IPV4 Default Gateway on Network Connection Details to assign an IP for meter.
3
2
1
For example,
Here the IPV4 Default Gateway is 192.168.1.1
You can assign an IP 192.168.1.145 for the meter

## Slide 7: 3. Configure meter communication settings
Open communication settings in front panel HMI
1)
1
Enter Setup on Home page of HMI
1
2
Press Tab button on meter front panel and turn to COMM setting page
3
Press Enter button and fill in the IP Address (P1/P2) assigned to the meter and IPV4 Default Gateway
2
3
4
Press Enter button again to confirm the modification.

## Slide 8: Verifying the Communication

## Slide 9: 1. Ping meter IP
Open communication settings in front panel HMI
·
WinKey + R on your keyboard. Or you could open the start menu and type Run.
1
2
Enter ping IP -t (Like ping 192.168.1.145 t) in the Run Command box followed by the Return key.
3
You can see the reply message on a command window if communicating with meter successfully.
3
1
2

## Slide 10: 2. Troubleshooting
No reply when ping meter IP
·
Check is there any problem with the Ethernet cable.
1
2
Check whether the meter gateway is the same with the server’s

## Slide 11: Thank You
Nathan
20180322